## Slide 1: Dynamic Trunking Protocol (DTP) & VLAN Trunking Protocol (VTP)
Understanding their Purpose, Usage, and Relevance Today

## Slide 2: What is DTP?
• DTP (Dynamic Trunking Protocol) is a Cisco proprietary protocol.
• It automatically negotiates trunking between two switches.
• Helps form trunk links dynamically without manual configuration.
• Common modes: dynamic auto, dynamic desirable, trunk, and access.

## Slide 3: Why DTP was Used
• Simplifies trunk configuration — no need to manually set trunk mode.
• Makes it easier for switches to connect and share VLAN traffic.
• Reduced setup time in older Cisco-only networks.

## Slide 4: Why DTP is Rarely Used Now
• Security risk — automatic negotiation can be exploited by attackers.
• Unauthorized devices can gain trunk access.
• Modern best practice: manually configure trunking and disable DTP.
• Use ‘switchport nonegotiate’ command to disable DTP.

## Slide 5: What is VTP?
• VTP (VLAN Trunking Protocol) is another Cisco proprietary protocol.
• It helps manage VLAN configurations across multiple switches.
• VTP propagates VLAN information (like names and IDs) from one switch to others.
• Modes: Server, Client, and Transparent.

## Slide 6: Why VTP was Used
• Centralized VLAN management — configure VLANs once, apply everywhere.
• Reduces administrative overhead.
• Ideal for large Cisco networks with many switches.

## Slide 7: Why VTP is Rarely Used Today
• Can cause major network outages if VLAN database is overwritten.
• Risk of VLAN deletion due to version mismatches or misconfigurations.
• Modern practice: manually manage VLANs or use automation tools.

## Slide 8: Modern Best Practices
• Manually configure VLANs and trunk ports for better control.
• Disable DTP using ‘switchport nonegotiate’.
• Use VTP Transparent mode or avoid VTP entirely in multi-vendor networks.
• Use network automation tools for consistency and accuracy.

## Slide 9: Summary
• DTP and VTP were designed to simplify VLAN and trunk configuration.
• Both are Cisco proprietary and were useful in older environments.
• Security and stability issues led to reduced use today.
• Modern networks rely on manual configuration and automation instead.