## Slide 1: OSPF Deep Dive — Full Detailed Version
Simple and beginner‑friendly detailed explanation

## Slide 2: What is OSPF?
OSPF = Open Shortest Path First, a link‑state routing protocol.
Routers exchange LSAs to build a full map of the network.
Runs SPF (Dijkstra) to find the shortest path.
Vendor‑neutral and used in IPv4 & IPv6 networks.

## Slide 3: Why OSPF Exists
RIP was slow and not scalable.
OSPF offers fast convergence and hierarchical design.
Uses event-based updates instead of periodic full updates.
Designed for medium and large networks.

## Slide 4: How OSPF Works
1. Routers send Hello packets.
2. Exchange LSAs (link-state advertisements).
3. Build identical LSDB (Link State Database).
4. Run SPF to compute best routes.

## Slide 5: OSPF Neighbor States
Down → Init → 2-Way → ExStart → Exchange → Loading → Full
Routers gradually synchronize their LSDB.
Full = neighbors fully synchronized.

## Slide 6: OSPF Areas
Areas reduce LSDB size and SPF calculations.
Area 0 = backbone and mandatory.
All other areas must connect to Area 0.
Improves network scalability.

## Slide 7: Area Types
Normal Area: all LSAs allowed.
Stub: blocks external Type‑5 LSAs.
Totally Stubby: only default route present.
NSSA: limited external routes via Type‑7 LSAs.

## Slide 8: LSAs (Link State Advertisements)
LSAs describe routers, networks, and routes.
Flooded reliably using LSU + acknowledgements.
All LSAs form the LSDB for an area.

## Slide 9: Important LSA Types
Type 1 — Router LSA.
Type 2 — Network LSA (from DR).
Type 3 — Summary LSA (ABR).
Type 4 — ASBR Summary LSA.
Type 5 — External LSAs.
Type 7 — NSSA external LSAs.

## Slide 10: DR & BDR
Used on multi-access networks (LAN/Ethernet).
DR reduces LSA flooding; BDR is backup.
Election: highest priority → highest router ID.

## Slide 11: OSPF Metric (Cost)
Lower cost = preferred path.
Cost = reference bandwidth / interface bandwidth.
Example: 100 Mbps → cost 1.

## Slide 12: OSPF Route Types
Intra-area: within same area (best).
Inter-area: between areas (via ABR).
E1: internal + external cost.
E2: only external cost.

## Slide 13: Virtual Links
Used when an area doesn't directly connect to Area 0.
Creates a logical tunnel through another area.
Useful temporarily during migrations.

## Slide 14: OSPF Security
Supports no-auth, simple password, MD5.
OSPFv3 uses IPsec for authentication.
Prevents rogue routers from forming adjacencies.

## Slide 15: OSPF Timers
Hello interval: 10 seconds.
Dead interval: 40 seconds.
Timers must match between neighbors.

## Slide 16: Route Redistribution
Imports routes from EIGRP, BGP, RIP, static.
Creates Type‑5 or Type‑7 LSAs.
Must be done carefully to avoid loops.

## Slide 17: Summarization
Done at ABR/ASBR.
Reduces LSDB size and improves stability.
Helps prevent unnecessary SPF recalculations.

## Slide 18: OSPFv3 (IPv6)
Supports IPv6 routing.
Authentication via IPsec.
Per‑link adjacency model.
Same SPF concepts but updated LSAs.

## Slide 19: Troubleshooting Commands
show ip ospf neighbor
show ip ospf database
show ip ospf interface
show ip route ospf

## Slide 20: Common Issues
Neighbors not forming → timer/auth mismatch.
LSA flaps → unstable link.
Missing routes → summarization or filtering issue.
Wrong DR → adjust interface priority.

## Slide 21: Final Summary
OSPF builds a full network map using LSAs.
SPF calculates best routes.
Areas provide scalability.
Reliable, scalable and widely used in enterprise networks.