## Slide 1: RIP & EIGRP Routing Protocols (Improved Version)
Beginner-friendly explanation with simple real-world examples

## Slide 2: What is RIP?
• RIP = Routing Information Protocol
• One of the oldest dynamic routing protocols
• Uses hop count to decide best path
• Maximum of 15 hops allowed
• Good for very small networks

## Slide 3: How RIP Works (Simple Explanation)
Imagine routers passing messages through nearby routers.
• Every router tells neighbors what networks it knows
• Neighbors update their routing tables
• Chooses shortest hop path
• Sends full updates every 30 seconds
ASCII Path Example: A → B → C → Destination

## Slide 4: RIP Versions
• RIPv1 – Classful, outdated
• RIPv2 – Classless, supports VLSM and authentication
• RIPng – RIP for IPv6 networks
• RIPv2 is most commonly used where RIP is needed

## Slide 5: Why RIP Is Rare Today
• Slow convergence
• Hop limit = 15 makes networks unscalable
• Prone to loops
• Mostly used today for labs, training, or old systems

## Slide 6: What is EIGRP?
• EIGRP = Enhanced Interior Gateway Routing Protocol
• Cisco-proprietary (now partially open)
• More advanced than RIP
• Uses multiple metrics: bandwidth, delay, load, reliability
• Ideal for medium and large networks

## Slide 7: How EIGRP Works (Simple Explanation)
Think of EIGRP as a smart GPS for routers.
• Uses hello packets to find neighbors
• DUAL algorithm ensures loop-free paths
• Sends only partial updates, not full tables
• Has backup routes ready → fast failover
ASCII Logic: Neighbor → Exchange Info → Best Path → Backup Path

## Slide 8: EIGRP Terminology (Simplified)
• Successor – Best path
• Feasible Successor – Backup path
• Feasible Distance – Local metric to destination
• Reported Distance – Neighbor’s metric
• DUAL uses these to ensure reliable routing

## Slide 9: Advantages of EIGRP
• Very fast convergence
• Loop-free routing
• Supports unequal load balancing
• More scalable than RIP
• Suitable for enterprises with Cisco devices

## Slide 10: RIP vs EIGRP
RIP:
• Simple
• Hop count only
• Max 15 hops
• Slow
• Small networks only
EIGRP:
• Advanced metrics
• Very fast
• Scalable
• Backup paths available
• Medium & large networks

## Slide 11: Where RIP & EIGRP Are Used Today
RIP:
• Old networks
• Student labs
EIGRP:
• Cisco-heavy networks
• Some enterprise deployments
But OSPF is preferred today because:
• Vendor-neutral
• Highly scalable
• Suitable for large organizations

## Slide 12: Summary
• RIP = simple but outdated
• EIGRP = faster, smarter, more scalable
• Both build routing tables automatically
• RIP is rare now; EIGRP still used but OSPF is growing
• Knowing both helps build strong routing fundamentals