## Slide 1: Introduction to Cisco Routers
Cisco routers are networking devices used to connect multiple networks together. They forward data packets based on IP addresses, acting as a traffic manager. Routers are found in homes, offices, and large enterprises for stable internet connectivity.

## Slide 2: Series of Cisco Routers
Cisco offers various router series depending on the use case:
- 800 Series: For small offices or homes.
- 1900/2900 Series: For medium-sized businesses.
- 3900/ASR Series: For large enterprises and ISPs.
Each series differs in speed, scalability, and features.

## Slide 3: External Router Hardware Components
These are the visible parts of a router that allow physical connections:
- Ethernet Ports for network cables.
- Power Port for electricity.
- Console and AUX Ports for configuration.
Example: Just like different plugs in a power board connect to various devices.

## Slide 4: Interface Ports
Interface ports are connectors that link the router to external devices and networks. They may be GigabitEthernet or FastEthernet. Each port has a unique label, for example, GigabitEthernet0/1 represents Module 0, Port 1.

## Slide 5: WIC and NM Slots
WIC (WAN Interface Card) slots are used to add new WAN connectivity options such as DSL or serial lines. NM (Network Module) slots expand router functionality — for example, adding VPN support or more Ethernet ports. Think of them as expansion slots like in a desktop computer.

## Slide 6: Ethernet, Power, Console, and AUX Ports
• Ethernet Port – For network cables to connect to LAN/WAN.
• Power Port – Supplies electrical power.
• Console Port – Used for initial configuration using command line.
• AUX Port – Often used for remote configuration through modems.

## Slide 7: Interface Port Numbering System
Cisco routers label their ports systematically, like FastEthernet0/0 or GigabitEthernet1/1. The first number represents the interface module, and the second number is the specific port. This helps network engineers easily identify connections.

## Slide 8: Internal Components of Cisco Routers
Routers work like computers — they have CPU, memory, storage, and a motherboard. Each component has a role in storing, processing, or booting configurations. Example: When powered on, the router loads its OS (Cisco IOS) from Flash memory into RAM.

## Slide 9: RAM (Random Access Memory)
RAM temporarily stores routing tables and the running configuration. All data in RAM is erased when the router is rebooted. Example: Similar to your PC's temporary workspace while you’re multitasking.

## Slide 10: NVRAM (Non-Volatile RAM)
NVRAM stores the startup configuration — the file loaded when the router boots. This memory remains intact even when power is off, like a car’s memory for saved radio stations.

## Slide 11: Flash Memory
Flash stores the router’s operating system (Cisco IOS) and backups. It’s non-volatile, meaning data stays even after reboot. Example: Similar to a USB drive that stores your software and files.

## Slide 12: ROM (Read-Only Memory)
ROM contains the router’s bootstrap program, responsible for powering on and loading the IOS. It also holds diagnostic code for hardware testing. Think of it like the BIOS in a PC that helps it start.

## Slide 13: Motherboard and CPU
The motherboard connects all components, while the CPU executes routing processes and protocols. Together, they are like the router’s brain and nervous system — handling data flow and logic decisions.

## Slide 14: SMPS (Switched-Mode Power Supply)
SMPS converts high-voltage AC into low-voltage DC power for internal components. It provides stable power output and protects circuits from fluctuations. Example: Like the power supply in your desktop computer.