## Slide 1: Router IOS and Routing Concepts
A complete guide to Cisco Router IOS and Routing Fundamentals

## Slide 2: Router IOS Fundamentals
Cisco IOS (Internetwork Operating System) is the software used to control and manage Cisco routers and switches.
Connection Methods:
• Console Cable – Direct connection to the router for configuration.
• AUX Connection – Remote access through a modem.
• Putty Software – A terminal emulator used to connect to routers and switches via serial or SSH.
• Packet Tracer – Cisco’s simulation software to practice network configurations.
These tools allow engineers to interact with routers for setup, testing, and troubleshooting.

## Slide 3: Understanding IOS Modes and Commands
Cisco IOS operates in multiple modes, each giving a different level of control:
• User EXEC Mode – Basic monitoring, limited access.
• Privileged EXEC Mode – Full monitoring and troubleshooting.
• Global Configuration Mode – Used to configure device-wide settings.
Common Commands:
• show – Displays information (e.g., show ip interface brief).
• copy – Copies configuration or system files.
• erase/delete – Removes configuration files.
• help – Provides syntax and command guidance.

## Slide 4: Router Boot Process, Security, and Backup
Router Boot Process:
1. POST (Power-On Self-Test) checks hardware.
2. Bootstrap loads the IOS image from flash.
3. Configuration loaded from NVRAM.
Router Security:
• Configure passwords for console, enable, and VTY lines.
• Use ROMMON mode for recovery in emergencies.
Backup & Recovery:
• Save configuration files to a TFTP server.
• Restore IOS image from TFTP during recovery.
• Always maintain a backup copy of the running configuration.

## Slide 5: Routing Concepts
Routers forward packets between different networks based on IP addresses.
Types of Routing:
• Static Routing – Administrator manually adds routes.
• Dynamic Routing – Routers exchange routes using routing protocols.
• Default Routing – Used when no specific route is found.
Static Routing Example:
Router(config)# ip route 192.168.2.0 255.255.255.0 10.0.0.2

## Slide 6: Dynamic Routing
Dynamic routing protocols automatically learn and update routes when network topology changes.
Key Concepts:
• Metric – A value that determines the best path (e.g., hop count, bandwidth).
• Routing Algorithm – Determines how paths are calculated (e.g., Dijkstra, Bellman-Ford).
• AS Number – Identifies a group of networks under one organization.
• Administrative Distance (AD) – Used to choose between multiple routing sources.
Routing Types:
• Interior Routing (within AS): OSPF, RIP, EIGRP.
• Exterior Routing (between AS): BGP.
Example: OSPF dynamically calculates the shortest path using cost metrics.