## Slide 1: RIP, EIGRP, OSPF, and Switch Hardware
Comprehensive Overview of Routing Protocols and Switch Components

## Slide 2: RIP Protocol
• RIP (Routing Information Protocol) is a distance-vector routing protocol that uses hop count as a metric.
• Terminology: Hop Count, Routing Table, Route Poisoning.
• RIP Timers: Update, Invalid, Hold-down, and Flush timers.
• Route Poisoning: Prevents routing loops by advertising unreachable routes.
• Practical Configuration:
- Enable RIP using ‘router rip’ command.
- Assign networks to RIP using ‘network <IP>’.
• Testing involves verifying routes using ‘show ip route’ and ‘debug ip rip’.

## Slide 3: EIGRP Protocol
• EIGRP (Enhanced Interior Gateway Routing Protocol) is an advanced distance-vector protocol.
• Uses DUAL (Diffusing Update Algorithm) for loop-free and efficient routing.
• Terminology: RTP (Reliable Transport Protocol), AS-number (Autonomous System number).
• Timers: Hello and Hold timers manage neighbor relationships.
• Practical Configuration:
- Enable EIGRP: ‘router eigrp <AS-number>’
- Assign networks using ‘network <IP>’
• Testing: Use ‘show ip eigrp neighbors’ and ‘show ip route eigrp’.

## Slide 4: OSPF Protocol
• OSPF (Open Shortest Path First) is a link-state routing protocol using Dijkstra’s algorithm.
• Terminology: DR (Designated Router), BDR (Backup Designated Router), Router-ID, Area Code.
• Works with Areas to optimize routing: Area 0 is the backbone area.
• Timers: Hello and Dead timers maintain adjacency.
• Practical Configuration:
- Enable OSPF: ‘router ospf <process-id>’
- Assign networks: ‘network <IP> area <area-id>’
• Testing: Use ‘show ip ospf neighbor’ and ‘show ip route ospf’.

## Slide 5: Switch Hardware
• Switches are hardware devices that connect multiple devices within a LAN.
• Internal Components:
- RAM: Stores running configuration and tables.
- NVRAM: Stores startup configuration.
- FLASH: Contains the Cisco IOS software.
- ROM: Used for boot diagnostics and recovery.
- CPU: Handles switching operations and packet processing.
- Motherboard: Connects all components together.
- SMPS (Switched Mode Power Supply): Provides regulated power.
• Switches operate mainly at Layer 2 (Data Link Layer) but some are Layer 3 switches supporting routing.