## Slide 1: Quality of Service (QoS)
Simple & Student-Friendly Explanation

## Slide 2: What is QoS?
QoS = Quality of Service.
Used to give priority to important network traffic.
Helps ensure smooth voice, video, and real‑time applications.
Prevents lag during heavy network usage.

## Slide 3: Why QoS is Needed (VoIP Example)
Voice calls need low delay and stable connection.
Without QoS, voice becomes choppy during congestion.
QoS ensures voice packets get priority.
Also important for gaming, video meetings, CCTV, etc.

## Slide 4: Traffic Classification
Classifying data into groups (voice, video, browsing, downloads).
Allows the network to handle each type differently.
Example: Voice = highest priority, browsing = normal.
Classification is the first step before applying QoS rules.

## Slide 5: Priority Marking (IPP & DSCP)
IPP (older system) marks packets with 0–7 priority values.
DSCP (modern system) uses 0–63 values for fine control.
Higher DSCP value = higher priority.
Routers treat DSCP‑marked packets differently.

## Slide 6: Queue Management
Routers create queues when traffic is high.
Important packets (voice/video) go to fast queues.
Less important packets wait in slower queues.
Prevents delays for real‑time traffic.

## Slide 7: Policing vs Shaping
Policing: Enforces speed limit; drops extra packets.
Shaping: Slows traffic smoothly using buffering.
Example: ISPs police speeds (hard limit).
Companies shape downloads to protect VoIP quality.

## Slide 8: Trusted Boundary
Point where the network trusts packet markings.
Usually the access switch marks IP phone traffic.
Prevents users from marking their traffic as 'high priority'.
Ensures QoS labeling remains honest across the network.

## Slide 9: Summary
QoS gives priority to important traffic like voice/video.
Uses classification, marking, queuing, policing, shaping.
DSCP is the main marking method today.
Essential for VoIP, video calls, gaming, and smooth networks.