## Slide 1: Spanning Tree Protocol (STP)
Easy and student-friendly explanation

## Slide 2: What is STP?
STP = Spanning Tree Protocol.
Prevents network loops in switching networks.
Loops cause broadcast storms and MAC table instability.
STP blocks extra paths to ensure only one active path exists.

## Slide 3: Why Loops Are Dangerous
Switches flood broadcast frames.
If loops exist, frames circulate endlessly.
High CPU & bandwidth usage → network crash.
STP breaks loops automatically.

## Slide 4: How STP Works (Simple)
1. Elects a Root Bridge.
2. Calculates the shortest path from each switch to Root.
3. Selects forwarding ports and blocks redundant ones.
4. Recalculates if a link fails → restores backup path.

## Slide 5: Root Bridge
Central switch chosen by lowest Bridge ID (priority + MAC).
Acts as the reference point for all path calculations.
Admins can manually set priority to choose the Root Bridge.

## Slide 6: Port Roles in STP
Root Port → best path to Root Bridge.
Designated Port → forwards traffic on each segment.
Blocked Port → prevents loops; backup path.
Only Root & Designated ports forward traffic.

## Slide 7: STP Timers
Hello Time: 2 seconds (BPDU send interval).
Forward Delay: 15 seconds.
Max Age: 20 seconds.
Total convergence: ~30–50 seconds.

## Slide 8: BPDU — STP Messages
BPDU = Bridge Protocol Data Unit.
Used for Root election, path selection, and loop detection.
If BPDU from Root is lost → network recalculates STP.

## Slide 9: Types of STP
STP (802.1D) — original, slow.
RSTP (802.1w) — rapid spanning tree, much faster.
MSTP (802.1s) — supports multiple spanning trees for VLANs.
Modern networks mostly use RSTP or MSTP.

## Slide 10: Simple Real-Life Example
Three switches forming a triangle → creates a loop.
STP blocks one link, forming a loop-free tree.
If active link fails, STP unblocks backup link.
Provides safe redundancy without loops.

## Slide 11: Summary
STP prevents broadcast loops in switched networks.
Uses BPDU to elect Root and choose forwarding paths.
Blocks redundant links and activates them on failure.
RSTP improves speed and is used in modern networks.